## Slide 1: Arduino Tutorial

## Slide 2: Sketch Structure
void setup()
void loop()

## Slide 3: Variables
HIGH, LOW
INPUT, OUTPUT, INPUT_PULLUP

## Slide 4: Built-in Functions

## Slide 5: Math
int constrain(x, a, b) // x = [a, b]
long map(value, fromLow, fromHigh, toLow, toHigh)

## Slide 6: Digital I/O
pinMode(pin, mode=[INPUT, OUTPUT, INPUT_PULLUP])
digitalWrite(pin, value=[HIGH, LOW])
int digitalRead(pin) // write HIGH to inputs to use pull-up resistors

## Slide 7: Analog I/O
analogReference(type=[DEFAULT, INTERNAL, EXTERNAL])
int analogRead(pin) // [0~1023], call twice if switching pins from high Z source
analogWrite(pin, value=[0~255]) // PWM

## Slide 8: Advanced I/O
unsigned long pulseIn(pin, [HIGH, LOW]) // [10ms, 3min]
unsigned long pulseIn(pin, [HIGH, LOW], timeout_in_ms)
unsigned long pulseIn(pin, [HIGH, LOW]) // [10ms, 3min]
unsigned long pulseIn(pin, [HIGH, LOW], timeout_in_ms)
tone(pin, frequency_in_Hz) // square wave
tone(pin, frequency_in_Hz, duration_in_ms)
noTone()
shiftOut(dataPin, clockPin, [MSBFIRST, LSBFIRST], value_in_byte)
byte shiftIn(dataPin, clockPin, , [MSBFIRST, LSBFIRST])

## Slide 9: Time
delay(ms)
delayMicroseconds(us)
unsigned long millis()
unsigned long micros()

## Slide 10: External Interrupts
attachInterrupt(digitalPinToInterrupt(pin), InterruptServiceRoutine, mode=[LOW, CHANGE, RISING, FALLING])
detachInterrupt(digitalPinToInterrupt(pin))
noInterrupts() // disables interrupts
interrupts() // re-enables interrupts

## Slide 11: Communication
Serial
  begin([300,1200,2400,4800,9600,14400,19200,28800,38400,57600,115200])
  end()
  int available()
  int read()
  flush()
  print()
  println()
  write()

## Slide 12: Libraries

## Slide 13: Standard Libraries
EEPROM
Servo
SoftwareSerial
Wire

## Slide 14: References
https://www.arduino.cc/reference/en/
https://dlnmh9ip6v2uc.cloudfront.net/learn/materials/8/Arduino_Cheat_Sheet.pdf